## Slide 1: Assimilation of Point and/or Spatial Data
Bailian Chen
EES-16
08/06/2020

## Slide 2: Recap: History matching point data
The variability in the predictions of CO2 S. is reduced by assimilating monitoring data after different monitoring durations
The reduction in variability increases with increased monitoring data assimilation

## Slide 3: Recap: History matching point data

## Slide 4: Recap: History matching point data

## Slide 5: Recap: History matching point data
Uncertainty reduction in risk quantities based on assimilation of point data is significant.
Will spatial data (e.g., spatial CO2 saturations from seismic) bring in additional benefits for uncertainty reduction?

## Slide 6: History matching CO2 plume area (spatial data)
Seismic data was converted to spatial CO2 saturation data
Manual history matching!!!
(Literature review)

## Slide 7: History matching CO2 plume area (spatial data)
Seismic data was converted to spatial CO2 saturation data
Manual history matching!!!
(Literature review)

## Slide 8: History matching CO2 plume area (spatial data)
Seismic data was converted to spatial CO2 saturation data
Manual history matching!!!
(Literature review)

## Slide 9: Should we conduct assisted history matching?
Approach: Use ES-MDA to assimilate time-varying spatial CO2 saturation data (from 4D seismic) into reservoir model
Outcomes: History matched simulated and observed spatial CO2 saturation data; updated reservoir permeability and porosity fields
How: Use all the gridblock by gridblock saturation data within the plume area? Similar like placing a monitoring well at each gridblock within the plume extent
Challenge: The number of data may be too big for a large scale reservoir with millions of gridblocks. Potential solutions:
  use representative point data;
  data reduction approach like randomized geostatistical approach (RGA) proposed by Lin et al. (2017).
CO2 plume
Ground truth

## Slide 10: Joint assimilation of spatial data and point data
Available data: time varying spatial CO2 saturations from seismic survey and point pressures from monitoring
Add point saturation/pressure data into spatial data set for joint assimilation

## Slide 11: Directly from seismic data
Seismic data (P-impedance) Reservoir simulation responses
PEM

## Slide 12: Directly from seismic data
Seismic data (P-impedance) Reservoir simulation responses
PEM
PEM model based on Gassmann equation (1951)
K: bulk modulus
G: shear modulus
HS: Hashin-Shtrikman

## Slide 13: Directly from seismic data

## Slide 14: Spatial data assimilation: Case study
Same synthetic example as we used for our previous work
Ground truth

## Slide 15: CO2 saturation maps – 4D Seismic
3 yrs
5 yrs
1 yr
Observational data size: 51*51*1 (2601), 51*51*2, 51*51*3

## Slide 16: Pressure maps – InSAR
3 yrs
5 yrs
1 yr
Interferometric Synthetic Aperture Radar (InSAR) is an effective way to measure changes in land surface altitude. InSAR makes high-density measurements over large areas by using radar signals from Earth-orbiting satellites to measure changes in land-surface altitude at high degrees of measurement resolution and spatial detail (Galloway and others, 2000).

## Slide 17: Plans
Start from only 1 CO2 saturation map, then 2 maps and 3 maps.
Add pressure maps
Add point monitoring data
Compare with our results from point data assimilation: uncertainty in the predictions of pressure/saturation, plume area, model improvement, etc.

## Slide 18: Assimilation of 1-yr saturation map
1 yr

## Slide 19: Prior and updated models
Prior
Updated
R1
R2
R3
R4
Ground truth

## Slide 20: CO2 saturation maps – 4D Seismic
3 yrs
5 yrs
1 yr

## Slide 21: Model updating (R1)
3 yrs
5 yrs
1 yr
Prior
Ground Truth

## Slide 22: CO2 saturation plume history matching (1 yr)
Observational CO2 saturation map
History matched CO2 saturation map (R1)
Prior (R1)

## Slide 23: CO2 saturation plume history matching (3 yrs)
Observational CO2 saturation map
History matched CO2 saturation map (R1)
Prior (R1)

## Slide 24: CO2 saturation plume history matching (5 yrs)
Observational CO2 saturation map
History matched CO2 saturation map (R1)
Prior (R1)

## Slide 25: CO2 saturation plume prediction at 15 yrs (R1)
Prior map
“True” map
1 yr
3 yrs
5 yrs

## Slide 26: Pressure map history matching (5 yrs)
Observational pressure buildup map
History matched pressure buildup map (R1)
History match error tolerance: 0.01 MPA

## Slide 27: Model updating
Prior
Updated
R1
R2
R3
R4
Not surprising without well matched pressure map!

## Slide 28: Next
Assimilation of 1 yr or 1 mth pressure map
Tighten pressure history matching error tolerance: from 0.01 to 0.001 MPa?
Saturation maps: assimilation of time series maps (1 yr + 3 yrs, 1 yr + 3 yrs + 5 yrs)
5 yrs
1 yr
1 mth